## Slide 1: 7. Make a duster from wooden piece using carpentry tools.

## Slide 2: Introduction
Carpentry may be designed as the process of making wooden articles and components such as roots, floors, partitions, doors and windows. Carpentry involves cutting, shaping and fastening wood and other materials together to produce a finished product. Preparation of joints is one of the important operations in wood work.
Joinery denotes connecting the wooden parts using different points such as lap joints, mortise and teman joints, bridle joints, etc.

## Slide 3: Carpentry Tools
Carpentry tools are used to produce components to an exact size. The types of carpentry tools are as follows.
1. Marking tools
2.Measuring tools
3. Holding tools
4. Cutting tools
5.Planning tools
6.Boring tools
7. Striking tools
8.Miscellaneous tools

## Slide 4: Marking tools
It is used to marking lines parallel to the edges of a wooden piece. It consists of a square wooden stem with a sliding wooden stock on it. On the stem, a marking pin is attached which is made up of steel.
This stem is provided with a steel nail to scratch the surface of the work. It consists of two pins; the distance between the pins is adjustable. It is used to draw parallel lines on the stock.

## Slide 5: Measuring tools
The carpentry measuring tools are classified as follows
    1. Steel tape 2.Steel rule 3.Calipers
Steel tapes and steel rules are mainly used for measuring short and lengths in millimeters.
A try square is used for testing squareness and marking of joints.
A mitre square is used for marking and measuring an angle of 45 degree.
A bevel square is used for marking and listing angles between 0 degree to 180 degree.
Calipers
  Calipers are used for the precision measurement of cylindrical surface. Inside calipers are used for measuring outside diameter and outside calipers are used to measure inner diameter of a pipe

## Slide 6: Holding tools
The carpentry holding tools are shown in fig.

## Slide 7: Carpentry vice
A carpentry vice is the common work holding device. It consists of one fixed jaw and one movable jaw. Its one jaw is fixed to the side of the table while the other is movable by means of a screw and a handle.

## Slide 8: Bar clamp
  The bar clamp (or) sash cramps are generally used in pairs in glueing up operations at the final assembly of joinery work. It is made up of a steel bar of T-section, wine malleable iron fittings and a steel screw.

## Slide 9: G-cramp
G-cramp is made up of malleable iron with acme threads of high quality steel .It can be used for clamping small work when glueing up.

## Slide 10: Cutting Tools

## Slide 11: Saws
A saw is used to cut wood into pieces. There is different type of saws, designed to suit different purpose. A saw is specified by the length of its tooled edge. The following saws are used in the carpentry section.

## Slide 12: Rip Saw
The blade of rip saw is either straight or skew-backed. The teeth are so set that the cutting edge of this saw makes a steeper angle about 600

## Slide 13: Cross Cut saw
This is similar in shape of a rip saw. It is used to cut across the grain of the stock. The correct angle for cross cutting is 450.The teeth are so set that the saw kerf is wider than the blade thickness. This allows the blade to move freely in the cut without sticking.

## Slide 14: Tenon or back saw
A tenon saw is used for fine and accurate work. It consists of a very fine blade, which is reinforced with a rigid steel back. The teeth are shaped like those of cross cut saw.

## Slide 15: Chisels
Chisels are used for cutting and shaping wood accurately. Wood chisels are made in various blade widths, ranging from 3 to 50mm .Most of the wood chisels are made into tang type, having a steel shank which fits inside the handle.

## Slide 16: Firmer chisels
These are general purpose chisels and are used either by hand pressure or by a mallet. The blade of a firmer chisel is flat and their sloping face is at an angle 150 to 520

## Slide 17: Mortise Chisels
These are general purpose chisels and are used for cutting mortises above 9 mm wide. The blade of a firmer type in which they have a thicker section and a stronger neck. By means of this chisel we can apply more Leverage to remove waste wood from the mortise

## Slide 18: Bevel chisels
A bevel chisel is similar in construction to the firmer chisel. Its edges are bevelled to allow access to difficult corners. It has a blade with a bevelled back due to which it can enter sharp corners for finishing in dovetail joints.

## Slide 19: Planing Tools
In general, planes are used to produce flat surfaces on wood. The cutting blade used in a place is very similar to a chisel. The blade of a plane is fitted in a wood or metallic block at an angle

## Slide 20: DUSTER MAKING
AIM:
    To construct a duster from the given work piece:
  1. Jack plane. 2) Hand saw. 3) Steel rule. 4) Pencil 5) Marking Gauge. 5) Try square
APPLICATION:
Cross bars in a cot, shelves.
SUPPLIED MATERIAL SPECIFICATION:
Venteek wood of size 150 x 45 x 30
TOOLS REQUIRED:

## Slide 21
Firmer Chisel. 8) Cleaning brush. 9) Wooden mallet
SEQUENCE OF OPERATION:
1. Preparing. 2) Marking. 3) Cutting/Sawing. 4) Finishing
WORKING
PREPARING
Prepare the work piece as described in previous section with a length of 150mm, 45mm and 30mm
2. MARKING:
Adjust the marking gauge to 10mm and set out the distance from the same along all the four sides of the piece on the 30mm thick side from both ends b) Again, adjust the marking gauge to 5mm and set out distance along all the four sides of the piece c) Now mark a distance of 5mm perpendicular to these Jines on the 30mm x 45mm sides from both ends d) Mark a diagonal line on al the inner square thus formed.

## Slide 22
3. CUTTING I SAWING:
Hold the piece horizontally in a way such that the portion to be cut is just above the jaw. Use a hand saw to cut along the required line markings but slightly inside the line as shown in figure to the required 5mm dept Now using a firmer chisel take a series of cuts to remove the wood up to this 5mm depth Hold the piece again using a firmer chisel slantly chip off the wood from the along the material diagonal side.
4. FINISHING:
Take a series of small cuts delicately on both the side pieces to remove the excess wood. Obtain a fine finish of the socket and shoulder assembly joint and clear off the waste by wire brush

## Slide 24
RESULT:
The Duster was produced from the given work piece and assembled joint was submitted for evaluation